## Slide 1: Side Channel and Fault Attack Testing of Cryptosystems in the view of Dr AI
Debdeep Mukhopadhyay
Institute Chair Professor
(FIEEE, FNA, FASc, FNAE, FAAIA)
Secured Embedded Architecture Laboratory (SEAL)
Department of Computer Science and Engineering
IIT Kharagpur
debdeep@cse.iitkgp.ac.in
debdeep.mukhopadhyay@gmail.com

## Slide 2: Artificial Intelligence: Boon for Security Evaluations of Cryptosystems
Can be used to attack cryptographic implementation using side-channel information
  More efficient than standard statistical techniques
  Can even break efficient side-channel countermeasure implementation like masking
Can be used to evaluate fault attack countermeasures
  Aids to mount efficient fault attacks on cryptographic implementation
AI for Attacks
Image Source: Google Images
Targets insecure real-life implementation of provably secure cryptographic encryption

## Slide 3: Side Channel Attack: Targets Implementation
Plaintext
Time
Heat
Current
EM radiations
Leakage
Encryption
Trace Acquisition
Acquired Traces
Retrieved Secret Key
Side-Channel Attacks are performed through an indirect measurement of a computation result via an auxiliary mechanism
Analysis
These are covert channels that leak information which the designers of cryptographic algorithms did not consider
Image Source: Google Images

## Slide 4: Side-Channel Analysis Methods
Strongest form of side channel attacks
Requires an adversary to have access to an identical experimental device that he can program to his choice
The success of these attacks relies on the ability to model noise
Profiled Analysis
Side-Channel Analysis
Targets intermediate computation of the target device
  Typically the input or output of an S-Box.
Adversary generates hypothetical power trace of the target device with guessed key byte.
Secret key is obtained by correlating the hypothetical power trace with the actual power trace.
Non-Profiled Analysis
Profiled Device
(Open)
Target Device
(Close)
Target Device
(Close)
Image Source: Google Images

## Slide 5: Profiled Deep Learning based Attack
Known Key
Targeted
Operation
Unknown Key
H. Maghrebi et al., “Breaking cryptographic implementations using deep learning techniques.” SPACE 2016
Template attacks (profiled attacks) are based on the Gaussian Assumption of the leakage distribution
  Deep Learning-based approach relaxes the Gaussian Assumption
The acquired traces do not require any types of pre-processing (like trace synchronization, denoising, feature selection, feature extraction, etc.)
The deep learning model can combine multiple leakage points
  Works efficiently against masking-based countermeasures than classical statistical methods
Advantage of Deep Learning Approach
Profiling
Phase
Attack
Phase
Image Source: Google Images

## Slide 6: EstraNet: An Efficient Shift-invariant Transformer Network
Incorporates novel self-attention called GaussiP attention
  Has linear time & memory complexity
    Computationally scales to traces with lengths > 10K
  Shift-invariant
    Highly effective against several jitter based countermeasures
  Good at capturing long distance dependency
    Highly effective against masking countermeasures
  Sparse attention scores
    Makes it effective for attacking very long traces (lengths > 10K)
  Gaussian kernel
    Makes it highly effective against clock jitter countermeasures
Suvadeep Hajra, Siddhartha Chowdhury, Debdeep Mukhopadhyay:
EstraNet: An Efficient Shift-Invariant Transformer Network for Side-Channel Analysis. IACR Trans. Cryptogr. Hardw. Embed. Syst. 2024(1): 336-374 (2024)

## Slide 7: Non-Profiled Deep Learning based Attack
Benjamin Timon, " Non-Profiled Deep Learning-based Side-Channel attacks with Sensitivity Analysis." TCHES 2019.
Unknown Key
Targeted
Operation
The translation-invariance property of CNN to outperform non-profiled Correlation Power Attack
The sensitivity analysis reveals points of interests such as leakage and mask locations in the trace
Breaks masked implementation without the knowledge (order of masking) about the underlying implemented protection
Advantage of Deep Learning Approach
Trains a model for each possible key byte
Correct key produces best training
Image Source: Google Images

## Slide 8: Deep Learning-based Fault-Attack Leakage Assessment
PART II

## Slide 9: Fault Attacks on Block Ciphers
Attacks based on induction of faults during Encryption
First conceived in 1996 by Boneh, Demillo and Lipton
A single fault can reduce the AES Key Size to around 2^8 values.
A double fault can uniquely retrieve the Key!
Clock Glitch
Voltage Glitch
Laser Gun
Electromagnetic Emanation
Rowhammer
Fault Injection Techniques
Tunstall, Mukhopadhyay, “Differential Fault Analysis of the Advanced Encryption Standard using a Single Fault.” WISTP 2011.
AES-128
Image Source: Google Images

## Slide 10: Fault Propagation
f
f’
f’
2f’
f’
f’
3f’
Key component of a fault attack
Attack procedure changes according to the fault model
Random localized faults
  Bit/nibble/byte fault
  Most general model
Biased faults
  Device-dependent model
Instruction skip/modify.
Constant fault
  Stuck-at-0/1¸
Fault Models
8th Round
Sub-Byte
8th Round
Shift-Row
8th Round
Mix-Column
9th Round
Sub-Byte
9th Round
Shift-Row
9th Round
Mix-Column
10th Round
Sub-Byte
10th Round
Shift-Row

## Slide 11: Testing Block Ciphers for Fault Attacks
Several countermeasures exist
  Either extremely resource hungry
  Or not robust against all possible faults
    Broken!!!
Malicious faults are highly repeatable
Different fault models
No existing theory for countermeasure design and evaluation
Designs are evaluated in-house
No standard design style
Challenges
How do we know what is secure and what is not?
Image Source: Google Images

## Slide 12: Automated Leakage Assessment
Measure Mutual Information
  Challenging without detailed knowledge of the countermeasure scheme
Insight
  We do not require accurate estimate
  It is sufficient to know if it is non-zero
Solution
  Theory of Non-Interference
How to detect Leakage?
Condition for No-Leakage
General idea
  Mutual Information (MI) between the secrets and the observables should be zero
Plaintext variable must be kept fixed
Violating of any of these two conditions indicates leakage
We use the first one in this work.
Image Source: Google Images

## Slide 13: ALAFA: Automatic Leakage Assessment
Saha, Mukhopadhyay, DasGupta, "ALAFA: Automatic Leakage Assessment for Fault Attack Countermeasures." DAC 2019.
Keep the key and plaintext fixed
Constant fault model
  Strongest among all
  No leakage imply strong security
Fix two different fault values one at a time and simulate
Perform t-test on the outcome of the two simulations
A t-Test based Framework
Image Source: Google Images

## Slide 14: ALAFA: Automatic Leakage Assessment
Keep the key and plaintext fixed
Constant fault model
  Strongest among all
  No leakage imply strong security
Fix two different fault values one at a time and simulate
Perform t-test on the outcome of the two simulations
A t-Test based Framework
Formalization of leakage due to faults
Simple and Statistical
Similar to well-accepted Side-Channel Leakage assessment method TVLA
Simulation-based
Algorithm-agnostic
Advantages
Saha, Mukhopadhyay, DasGupta, "ALAFA: Automatic Leakage Assessment for Fault Attack Countermeasures." DAC 2019.

## Slide 15: Deep Learning for Leakage Assessment
t-test can only capture difference in statistical moments
  Sub-optimal.
  False-negatives
In side channel analysis (SCA), countermeasures like masking, the order of masking decides the maximum allowable leakage order
  In FA the leakage order depends on the fault propagation and not available a-priori to the tester.
  Security guarantee depends on the evaluator’s choice!
Issues with ALAFA
Deep Learning (DL) methods can be a powerful tool as it is renowned to learn in highly multi-variate scenarios and can take several complex inter-relations among different features.
DL does not need order-related information from the evaluator.
DL performs better in noisy scenarios compared to the t-test based approach.
Advantage of Deep Learning
Image Source: Google Images

## Slide 16: DL-FALAT: Deep Learning-based Automatic Leakage Assessment
Sayandeep Saha, Manaar Alam, Arnab Bag, Debdeep Mukhopadhyay, Pallab Dasgupta: Learn from Your Faults: Leakage Assessment in Fault Attacks Using Deep Learning. J. Cryptol. 36(3): 19 (2023)
Encryption
Faulty
Ciphertexts
F0
Faulty
Ciphertexts
F1
Dataset
Binary Labels
K-Fold
Cross-Validation
Validation
Accuracy
A0
A1
A2
AK-2
AK-1
H0: Xmean > 0.5
Is the accuracy result more than a random guess?
Learning need not require to be the “best”
A small indication of leaning is sufficient to decide leakage
Observation
Start with small sample size of 500
Perform the training and validation
  Stratified K-fold cross validation with K=50
  Good for preventing overfitting
One-sided t-test over the cross-validation accuracies
Increase the sample size if no leakage is detected
Decision Making
Image Source: Google Images

## Slide 17: Results on Leakage Detection
Infective Countermeasure
B. Gierlichs et al., "Infective computation and dummy rounds: fault protection for block ciphers without check-before-output." LatinCrypt 2012.
Noise-Free
Noisy
RIMBEN Countermeasure
B. Wang et al., "Exploration of benes network in cryptographic processors: A random infection countermeasure for block ciphers against fault attacks." IEEE TIFS 2016.
False negative for t-test but DL-FALAT detects leakage
128th order statistical moment – data complexity for t-test would be very high

## Slide 18: Results on Leakage Detection
SIFA Countermeasure
Saha, Jap, BasuRoy, Avik Chakraborty, Bhasin,Mukhopadhyay,"A framework to counter statistical ineffective fault analysis of block ciphers using domain transformation and error correction." IEEE TIFS 2019.
Detection Countermeasure
1-bit Parity
R. Shahmirzadi et al., "Impeccable Circuits II." IACR Cryptology ePrint Archive 2019.
AntiSIFA
Impeccable Circuit II

## Slide 19: Take-away
Deep Learning can aid an adversary/tester to compromise/assess the security of a cryptographic implementation using power side-channel
  More efficient than classical statistical approaches in terms of number of attack traces
  Also efficient against masking-based countermeasures
Deep Learning can aid an adversary/tester to compromise/assess the fault-attack leakage of a cryptographic implementation
  More efficient than t-test based approach in terms of number of ciphertexts
  Less false negatives and easy to interpret leakage order

## Slide 20: AI for Implementation Security : The Way Forward
Pertinent questions facing the implementation security community for AI adoption:

## Slide 21: AI for Implementation Security : The Way Forward
Pertinent questions facing the implementation security community for AI adoption:
Lack of documentation for AI specific pitfalls in implementation security context
  How to pre-process data (like side-channel traces) to render them training friendly ?
  How to avoid overfitting ?
  Which architectures to use for what use-cases? Is deep = better?
  How to ensure quality of training data? Issues like class imbalance, requisite amount of data.
  Is the inference result interpretation reliable (like high accuracy, but on unbalanced data) ?
Not all implementation security engineers may know ML internals/details to take decisional calls on these issues

## Slide 22: AI for Implementation Security : The Way Forward
Pertinent questions facing the implementation security community for AI adoption:
Lack of documentation for AI specific pitfalls in implementation security context
Need for suggestive guidelines/procedures for ensuring research portability
  Statistical tests (like CPA) are inherently portable. But what about ML models?
  Can a ML model for testing leakage on Arduino Uno be reused for testing leakage on Raspberry Pi?
  Educate testers on ML transfer learning. Again, lack of easy-to-access documentation for the same.

## Slide 23: AI for Implementation Security : The Way Forward
Pertinent questions facing the implementation security community for AI adoption:
Lack of documentation for AI specific pitfalls in implementation security context
Need for suggestive guidelines/procedures for ensuring research portability
Consensus on how we build upon each other’s research
  Statistical tests are algorithms; we publish the same, and anyone can use it.
  Trained ML models + collected datasets are often considered as IPs. Not everyone open-sources them!
  A lack of consensus on how to share models/datasets will create isolated islands in the implementation security community.

## Slide 24: AI for Implementation Security : The Way Forward
Pertinent questions facing the implementation security community for AI adoption:
Lack of documentation for AI specific pitfalls in implementation security context
Need for suggestive guidelines/procedures for ensuring research portability
Consensus on how we build upon each other’s research
Licensing !
  What is the goodwill policy of licensing a model for testing my implementation, that had been partially trained on dataset curated by somebody else?
  Consensus on licensing of such models, especially if they are transfer learned!

## Slide 25
Thank You
For any query please feel free to contact
Debdeep Mukhopadhyay: debdeep.mukhopadhyay@gmail.com